# Revision History

| Version | Date | Comments |
| --- | --- | --- |
| 0.1 |  | Initial |
| 0.2 | 10/26/2011 | Revised how we detect a totem via USB scanning. Depricated ATI0/Get ID String command |

# Overview

The Totem’s use a serial interface for the programming and status interface.  This document explains the protocol and command set

# Connection Properties

The serial connection supported is a 9600-8-N-1 connection.

# About the Protocol

## Usage

The protocol handles one command at a time in the Request-Response style.

## On Connection

In order to support the scanning of serial ports and detection of totems, the totem will emit the following string when a serial connection is made:

++TOTEM

www.mytribaltotem.com

## General Response Format

In order to easily match the request with a response, each response echoes the command with the prefix of “++”  This allows for a “handshaking” style of interface which is easier to manage pragmatically.

# Command Set

## Set Totem Code

Program the device with a given totem code

### Command

| Syntax | Example | Notes |
| --- | --- | --- |
| AT&S50=<totem code> | AT&S50=12355 | Totem code is a string w/out any quotations |

### Response

| Condition | Syntax | Notes |
| --- | --- | --- |
| Success | ++AT&S50++OK |  |
| Error | ++ERROR |  |

## Get Totem Code

Get the totem code that is stored in the totem

### Command

| Syntax | Example | Notes |
| --- | --- | --- |
| ATS50? | ATS50? |  |

### Response

| Condition | Syntax | Notes |
| --- | --- | --- |
| Success | ++ATS50++<totemcode> |  |
| Error | ++ERROR |  |

## Get ID String <DEPRICATED>

Returns a string that indicates the device is a totem.  This is commonly used when scanning serial connections where one has to determine if a valid serial connection (e.g. COM1) has a totem attached to it versus another USB device (e.g. a disk drive)

### Command

| Syntax | Example | Notes |
| --- | --- | --- |
| ATI0 | ATI0 |  |

### Response

| Condition | Syntax | Notes |
| --- | --- | --- |
| Success | ++ATI0++totem | Totem is a literal string that is returned by the device. |
| Error | ++ERROR |  |

## Get Software Version

Returns the version of software programmed in the totem

### Command

| Syntax | Example | Notes |
| --- | --- | --- |
| ATI1 | ATI1 |  |

### Response

| Condition | Syntax | Notes |
| --- | --- | --- |
| Success | ++ATI1++1.0 | Software version is 1.0 |
| Error | ++ERROR |  |

## Get Serial Protocol Version

Returns the version of the serial interface supported by the totem

NOT IMPLEMENTED YET

### Command

| Syntax | Example | Notes |
| --- | --- | --- |
| ATI2 | ATI2 |  |

### Response

| Condition | Syntax | Notes |
| --- | --- | --- |
| Success | ++ATI2++1.0 | Device uses version 1.0 of the serial protocol |
| Error | ++ERROR |  |

## Get Network Protocol Version

Returns the version of totem to totem network protocol that is supported by the totem

NOT IMPLEMENTED YET

### Command

| Syntax | Example | Notes |
| --- | --- | --- |
| ATI3 | ATI3 |  |

### Response

| Condition | Syntax | Notes |
| --- | --- | --- |
| Success | ++ATI3++1 | Device uses version 1 of the serial protocol |
| Error | ++ERROR |  |